CompatiCard II BIOS Notes -- Version 2.01 -- September 18, 1990


The following information is provided for programmers that need 
to access diskettes sectors directly.  This information is 
provided with no technical support for use by qualified 
programmers.  They are similar in function to the routines 
provided by the system BIOS which you should be familiar with.  

Any comments or suggestions should put in writing and sent Attn: 
Software Engineering.  Reasonable requests for additional 
functions may be incorporated into future versions.



        CompatiCard II BIOS Interrupt 13h Specifications


These functions are provided by the CompatiCard II BIOS 
(contained in CCDRIVER.SYS) when properly installed.  The 
CompatiCard II functions are similar to the system BIOS functions 
provided for floppy diskette I/O.  When an interrupt 13h function 
is requested, the CompatiCard II BIOS will look at the physical 
drive address specified and it will only process requests with 
valid addresses.  An address is valid if it was specified in the 
CCDRIVER.SYS line of the CONFIG.SYS file.  Any interrupt 13h 
requests that do not contain valid addresses will be ignored and 
passed to the system BIOS for processing.

Most of the functions return an error code in the AH register 
upon completion.  In addition, the carry flag (CY) will be set if 
the error code returned in AH is non-zero.  The error codes are 
defined as follows:

     AH = 00h  successful completion of operation
          80h  diskette drive was not ready
          40h  seek failure
          20h  general controller failure
          10h  data error (CRC) on diskette
          09h  attempt to DMA across 64K boundary
          08h  DMA overrun
          04h  sector not found
          03h  write protect error
          02h  address mark not found
          01h  bad command passed to driver
     
Some of the functions reference parameters that are kept in the 
BIOS diskette drive parameter table.  The table is pointed to by 
INT 1eh (0:78h).  The layout of the table is as follows:

     Offset  Size   Description

        0    byte   not used
        1    byte   not used
        2    byte   Number of timer ticks to keep motor on
        3    byte   bytes per sector (0=128, 1=256, 2=512, & 
                    3=1024)
        4    byte   number of sectors on a track (used only by 
                    the FORMAT function)
        5    byte   read/write/verify gap length
        6    byte   not used
        7    byte   format gap length
        8    byte   format fill byte
        9    byte   head settle time (in milliseconds)
       10    byte   motor startup time (in 1/8 seconds)

If your program needs to alter any of these parameters from their 
original values, you should copy the original table to a scratch 
area and re-point INT 1eh to the scratch area.  The alterations 
should be made to your copy of the table and not the original.  
Before your program terminates, you must restore INT 1eh back to 
the original table.


Functions:

 0 - reset disk system
          This function can be called after a disk error.  It is 
          not required because the CompatiCard II BIOS will 
          automatically perform a reset when needed.

          Entry:
               AH = 0
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
               CY = 1 if error
               AH = error code


 1 - Get I/O error code from last operation
          This function will return the status code from the last 
          I/O operation performed on the drive. 

          Entry:
               AH = 1
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
               CY = 1 if error
               AH = error code


 2 - Read sectors
          This function is used to read from a diskette.  It can 
          be used to read more than 1 sector but all of the 
          sectors to be read must be on the same track.  

          Entry:
               AH = 2
               AL = number of sectors to read (1-n)
               ES:BX = address of buffer
               CH = cylinder (0-n)
               CL = sector number
               DH = head (0-1)
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
               CY = 1 if error
               AH = error code
               AL = number of sectors successfully read

          Note: Sector size, motor on time, motor startup time, 
          head settle time, and gap length are obtained from the 
          BIOS diskette drive parameter table. 


 3 - Write sectors
          This function is used to write to a diskette.  It can 
          be used to write more than 1 sector but all of the 
          sectors to be written must be on the same track.  

          Entry:
               AH = 3
               AL = number of sectors to write (1-n)
               ES:BX = address of buffer
               CH = cylinder (0-n)
               CL = sector number
               DH = head (0-1)
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
               CY = 1 if error
               AH = error code
               AL = number of sectors successfully written

          Note: Sector size, motor on time, motor startup time, 
          head settle time, and gap length are obtained from the 
          BIOS diskette drive parameter table. 


 4 - Verify sectors
          This function is used to verify sectors from a 
          diskette.  It can be used to verify more than 1 sector 
          but all of the sectors to be verified must be on the 
          same track.  

          Entry:
               AH = 4
               AL = number of sectors to verify (1-n)
               CH = cylinder (0-n)
               CL = sector number
               DH = head (0-1)
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
               CY = 1 if error
               AH = error code
               AL = number of sectors successfully verified

          Note: Sector size, motor on time, motor startup time, 
          head settle time, and gap length are obtained from the 
          BIOS diskette drive parameter table. 


 5 - Format track
          This function is used to format a track on a diskette.  

          Entry:
               AH = 5
               ES:BX = ptr to buffer containing sector information
               CH = cylinder (0-n)
               DH = head (0-1)
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
               CY = 1 if error
               AH = error code

          Note: Sector size, format gap length, number of sectors 
          to format, and fill byte are obtained from the BIOS 
          diskette drive parameter table. 

          The sector information required for formatting is a 
          collection of four byte address fields.  There should 
          be one address field per sector being formatted.  Each 
          field is made up of four bytes, (C, H, R, N), where 
          C=track number, H=head number, R=sector number, and 
          N=number of bytes per sector (0=128, 1=256, 2=512, and 
          3=1024). 


 8 - Return drive parameters
          This function is used to return some parameters about 
          the specified drive. 

          Entry:
               AH = 8
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
                 AX = 0
                 BL - bits 7 to 4 = 0
                      bits 3 to 0 - drive type
                        0 = other type
                        1 = 360KB
                        2 = 1.2MB
                        3 = 720KB
                        4 = 1.44MB
                 BH = 0
                 CL = maximum sectors per track
                 CH = maximum number of cylinders
                 DL = number of primary drives installed
                 DH = maximum head number
              ES:DI = pointer to 11 byte diskette drive parameter
                      table associated with the maximum supported
                      media type for the drive specified
               CY = 1 if error
               AH = error code


 9 - Set CompatiCard parameters
          This function is used to set parameters for a diskette 
          drive.  Each physical drive get its own set of 
          parameters which are retained unless they are changed 
          using function 9 or DOS is re-booted.

          Entry:
               AH = 9
               AL = number of retries after I/O error (0-255)
               CH = double step flag (0=single step and  1=double 
                    step)
               CL = density (1=DD and 2=HD)
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
               CY = 1 if error
               AH = error code


 10 - Return CompatiCard parameters
          This function is used to return the parameters which 
          are currently set for a drive.  Since each drive gets 
          its own set of parameters, this function can return 
          different parameters according to the physical drive 
          address specified.

          Entry:
               AH = 10
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
                 AL = number of retries after I/O error (0-255)
                 CL = density (1=DD and 2=HD)
                 CH = double step flag (0=single step and  1=double 
                      step)
                 BL = diskette drive type (0-7)
                 BH = step rate (in milliseconds)
                 ES is altered on exit
               CY = 1 if error
               AH = error code


 11 - Return next sector ID
          This function is used to return the next sector ID read 
          from the diskette. 

          Entry:
               AH = 11
               CH = cylinder (0-n)
               CL = density (1=DD and 2=HD)
               DH = head (0-1)
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
                 AL = sector size (0=128, 1=256, ...)
                 CL = sector number
                 CH = cylinder number
                 DH = side
               CY = 1 if error
               AH = error code


 21 - Read DASD Type
          This function is used to return change line 
          availability information.  The disk change line is not 
          supported on the CompatiCard II and is simulated using 
          the  system clock.  This function will always return  a 
          "no change line" for a CompatiCard II drive.

          Entry:
               AH = 21
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
                 AL = 0  drive not defined
                      1  no change line
               CY = 1 if error
               AH = error code


 22 - Return change line status
          This function is used to return change line 
          status information.  The disk change line is not 
          supported on the CompatiCard II and is simulated using 
          the system clock.  A "not active" value will be 
          returned if it has been less than 2 seconds since the 
          last diskette operation to the drive.

          Entry:
               AH = 22
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if AH = 0
               CY = 1 if AH not 0
               AH = 0  change signal not active
                    6  change signal active


 23 - Set DASD type for format
          This function is used to set some parameters before a 
          format operation. This function is provided for system 
          BIOS compatibility.  The use of function 9 is preferred 
          for new programs.

          Entry:
               AH = 23
               AL = 1  360KB diskette in 360KB drive
                    2  360KB diskette in 1.2MB drive
                    3  1.2MB diskette in 1.2MB drive
                    4  720KB diskette in 720KB drive
               DL = physical drive address (0-15)

          Exit:
               CY = 0 if no error
               CY = 1 if error
               AH = error code


 24 - Set media type for format
          This function is used to set some parameters before a 
          format operation. This function is provided for system 
          BIOS compatibility.  The use of function 9 is preferred 
          for new programs.

          Entry:
               AH = 24
               CL = number of sectors per track
               CH = number of cylinders
               DL = physical drive address (0-15)

          Exit:
              ES:DI = pointer to 11 byte diskette drive parameter
                      table associated with the specified media
                      type
               CY = 0 if error code is 0
               CY = 1 if error code is not 0
               AH = error code